## Slide 1: CS162 Operating Systems and Systems Programming Lecture 9 Synchronization 3: Semaphores, Monitors and Readers/Writers
February 13th, 2024
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Atomic Instruction Operations
test&set (&address) { /* most architectures */ result = M[address]; // return result from “address” and M[address] = 1; // set value at “address” to 1 return result; }
swap (&address, register) { /* x86 */ temp = M[address]; // swap register’s value to M[address] = register; // value at “address” register = temp; // value from “address” put back to register return temp; // value from “address” considered return from swap }
compare&swap (&address, reg1, reg2) { /* x86 (returns old value), 68000 */ if (reg1 == M[address]) { // If memory still == reg1, M[address] = reg2; // then put reg2 => memory return success; } else { // Otherwise do not change memory return failure; } }
load-linked&store-conditional(&address) { /* R4000, alpha */ loop: ll r1, M[address]; movi r2, 1; // Can do arbitrary computation sc r2, M[address]; beqz r2, loop; }

## Slide 3: Recall: Implementing Locks with test&set
Simple lock that doesn’t require entry into the kernel:
// (Free) Can access this memory location from user space! int mylock = 0; // Interface: acquire(&mylock); // release(&mylock);
acquire(int *thelock) { while (test&set(thelock)); // Atomic operation! }
release(int *thelock) { *thelock = 0; // Atomic operation! }
Discussion:
  Can have as many locks as memory locations!
  If lock is free, only one thread will get to run test&set which reads 0 and sets lock=1
  If lock is busy, test&set reads 1 and sets lock=1 (no change) It returns 1, so while loop continues.
  When we set thelock = 0, someone else can get lock.
Busy-Waiting: thread consumes cycles while waiting
  For multiprocessors: every test&set() is a write, which makes value ping-pong around in cache (using lots of network BW)

## Slide 4: Better Locks using test&set
Can we build test&set locks without busy-waiting?
  Mostly. Idea: only busy-wait to atomically check lock value
Note: sleep has to be sure to reset the guard variable
  Why can’t we do it just before or just after the sleep?
release(int *thelock) { // Short busy-wait time while (test&set(guard)); if anyone on wait queue { take thread off wait queue Place on ready queue; } else { *thelock = 0; } guard = 0;
int guard = 0; // Global Variable!
int mylock = 1; // Interface: acquire(&mylock); // release(&mylock);
acquire(int *thelock) {
// Short busy-wait time while (test&set(guard)); if (*thelock == 1) {
put thread on wait queue;
go to sleep() & guard = 0 ????
// guard == 0 on wakup; } else { *thelock = 1; guard = 0; } }

## Slide 5: Analysis: Lock Implementation using interrupts
If one thread in critical section, no other activity (including OS) can run!
Lock argument not used!
Naïve Implementation
int mylock=0;
acquire(&mylock);
…
critical section;
…
release(&mylock);
acquire(int *thelock) {
disable interrupts; }
release(int *thelock) { enable interrupts; }
acquire(int *thelock) {
// Short busy-wait time disable interrupts; if (*thelock == 1) {
put thread on wait-queue;
go to sleep() //See Lecture 8! } else { *thelock = 1; enable interrupts; } }
release(int *thelock) { // Short busy-wait time disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { *thelock = 0; } enable interrupts; }
Desired API
Better Implementation

## Slide 6: Analysis: Lock Implementation using test&set
Threads waiting to enter critical section busy-wait!
int mylock=0;
acquire(&mylock);
…
critical section;
…
release(&mylock);
int mylock = 0;
acquire(int *thelock) {
while(test&set(thelock)); }
release(int *thelock) { *thelock = 0; }
int guard = 0; // global!
acquire(int *thelock) {
// Short busy-wait time while(test&set(guard)); if (*thelock == 1) {
put thread on wait-queue;
go to sleep()& guard = 0;
// guard == 0 on wakeup } else { *thelock = 1; guard = 0; } }
release(int *thelock) { // Short busy-wait time while (test&set(guard)); if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { *thelock = 0; } guard = 0; }
Naïve Implementation
Desired API
Better Implementation??

## Slide 7: Linux futex: Fast Userspace Mutex
uaddr points to a 32-bit value in user space
futex_op
  FUTEX_WAIT – if val == *uaddr sleep till FUTEX_WAIT
    Atomic check that condition still holds after we disable interrupts (in kernel!)
  FUTEX_WAKE – wake up at most val waiting threads
  FUTEX_FD, FUTEX_WAKE_OP, FUTEX_CMP_REQUEUE: More interesting operations!
timeout
  ptr to a timespec structure that specifies a timeout for the op
Interface to the kernel sleep() functionality!
  Let thread put themselves to sleep – conditionally!
futex is not exposed in libc; it is used within the implementation of pthreads
  Can be used to implement locks, semaphores, monitors, etc…
#include <linux/futex.h>
#include <sys/time.h>
int futex(int *uaddr, int futex_op, int val,
const struct timespec *timeout );

## Slide 8: Example: First try: T&S and futex
Properties:
  Sleep interface by using futex – no busywaiting
No overhead to acquire lock
  Good!
Every unlock has to call kernel to potentially wake someone up – even if none
  Slows down the uncontested case where only one thread acquiring and releasing over and over…!
int mylock = 0; // Interface: acquire(&mylock);
// release(&mylock);
acquire(int *thelock) {
while (test&set(thelock)) {
futex(thelock, FUTEX_WAIT, 1);
} }
release(int *thelock) {
*thelock = 0; // unlock futex(thelock, FUTEX_WAKE, 1);
}

## Slide 9: Example: Try #2: T&S and futex
This is syscall-free in the uncontended case
  Temporarily falls back to syscalls if multiple waiters, or concurrent acquire/release
But it can be considerably optimized!
  See “Futexes are Tricky” by Ulrich Drepper
release(int *thelock, bool *maybe) { *thelock = 0;
if (*maybe) {
*maybe = false;
// Try to wake up someone
futex(thelock, FUTEX_WAKE, 1);
} }
bool maybe_waiters = false;
int mylock = 0; // Interface: acquire(&mylock,&maybe_waiters);
// release(&mylock,&maybe_waiters);
acquire(int *thelock, bool *maybe) {
while (test&set(thelock)) {
// Sleep, since lock busy!
*maybe = true;
futex(thelock, FUTEX_WAIT, 1);
// Make sure other sleepers not stuck
*maybe = true;
} }

## Slide 10: Try #3: Better, using more atomics
Much better: Three (3) states:
  UNLOCKED: No one has lock
  LOCKED: One thread has lock
  CONTESTED: Possibly more than one (with someone sleeping)
Clean interface!
Lock grabbed cleanly by either
  compare&swap()
  First swap()
No overhead if uncontested!
Could build semaphores in a similar way!
typedef enum { UNLOCKED,LOCKED,CONTESTED } Lock;
Lock mylock = UNLOCKED; // Interface: acquire(&mylock);
// release(&mylock);
acquire(Lock *thelock) {
// If unlocked, grab lock!
if (compare&swap(thelock,UNLOCKED,LOCKED))
return;
// Keep trying to grab lock, sleep in futex
while (swap(thelock,CONTESTED) != UNLOCKED))
// Sleep unless someone releases here!
futex(thelock, FUTEX_WAIT, CONTESTED);
}
release(Lock *thelock) {
// If someone sleeping, if (swap(thelock,UNLOCKED) == CONTESTED)
futex(thelock,FUTEX_WAKE,1); }

## Slide 11: Recall: Where are we going with synchronization?
Hardware
Higher-level API
Programs
We are going to implement various higher-level synchronization primitives using atomic operations
  Everything is pretty painful if only atomic primitives are load and store
  Need to provide primitives useful at user-level
Load/Store Disable Ints Test&Set Compare&Swap
Locks Semaphores Monitors Send/Receive
Shared Programs

## Slide 12: Administrivia
Midterm This Thursday, 8-10pm (February 15)!
  In person: Dwinelle 155 (here) or VLSB 2050
    Look on ED for which room you should go to
  You are responsible for all materials up to and including today’s lecture!
    Including Semaphores and Monitors
    I have a complete version of the synchronization lectures available on YouTube from my Fall 2020 class. [Note – the names of the lectures have changed slightly!]
You get one (1) double-side page of handwritten notes
  Hand drawn figures, hand written notes
  No copying of figures directly from slides, no microfiche, etc
  Redraw them if you want them on your notes!
If you are sick, let us know.
  Do not come to the midterm!
No class on Thursday
  I will have extra office hours during class time
No section this week!
No OH on Monday (it is a holiday!)

## Slide 13: Producer-Consumer with a Bounded Buffer
Problem Definition
  Producer(s) put things into a shared buffer
  Consumer(s) take them out
  Need synchronization to coordinate producer/consumer
Don’t want producer and consumer to have to work in lockstep, so put a fixed-size buffer between them
  Need to synchronize access to this buffer
  Producer needs to wait if buffer is full
  Consumer needs to wait if buffer is empty
Example 1: GCC compiler
  cpp | cc1 | cc2 | as | ld
Example 2: Coke machine
  Producer can put limited number of Cokes in machine
  Consumer can’t take Cokes out if machine is empty
Others: Web servers, Routers, ….
Consumer
Consumer
Producer
Consumer
Buffer
Producer

## Slide 14: Bounded Buffer Data Structure (sequential case)
Insert: write & bump write ptr (enqueue)
Remove: read & bump read ptr (dequeue)
How to tell if Full (on insert) Empty (on remove)?
And what do you do if it is?
What needs to be atomic?
typedef struct buf {
int write_index;
int read_index;
<type> *entries[BUFSIZE];
} buf_t;
w
r
di
di+1
di+2

## Slide 15: Bounded Buffer – first cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {}; // Wait for a free slot
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {}; // Wait for arrival
item = dequeue(); release(&buf_lock);
return item
}
Will we ever come out of the wait loop?

## Slide 16: Bounded Buffer – 2nd cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {release(&buf_lock); acquire(&buf_lock);}
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {release(&buf_lock); acquire(&buf_lock);}
item = dequeue(); release(&buf_lock);
return item
}
What happens when one is waiting for the other?
- Multiple cores ?
- Single core ?


## Slide 17: Better Primitive: Semaphores
Semaphores are a kind of generalized lock
  First defined by Dijkstra in late 60s
  Main synchronization primitive used in original UNIX
Definition: a Semaphore has a non-negative integer value and supports the following operations:
  Set value when you initialize
  Down() or P(): an atomic operation that waits for semaphore to become positive, then decrements it by 1
    Think of this as the wait() operation
  Up() or V(): an atomic operation that increments the semaphore by 1, waking up a waiting P, if any
    This of this as the signal() operation
Technically examining value after initialization is not allowed.

## Slide 18: Semaphores Like Integers Except…
Value=2
Value=1
Value=0
Semaphores are like integers, except:
  No negative values
  Only operations allowed are P and V – can’t read or write value, except initially
  Operations must be atomic
    Two P’s together can’t decrement value below zero
    Thread going to sleep in P won’t miss wakeup from V – even if both happen at same time
POSIX adds ability to read value, but technically not part of proper interface!
Semaphore from railway analogy
  Here is a semaphore initialized to 2 for resource control:
Value=1
Value=0
Value=2
P()
V()

## Slide 19: Two Uses of Semaphores
Mutual Exclusion (initial value = 1)
Also called “Binary Semaphore” or “mutex”.
Can be used for mutual exclusion, just like a lock:
    semaP(&mysem); // Critical section goes here semaV(&mysem);
Scheduling Constraints (initial value = 0)
Allow thread 1 to wait for a signal from thread 2
  thread 2 schedules thread 1 when a given event occurs
Example: suppose you had to implement ThreadJoin which must wait for thread to terminate:
    Initial value of semaphore = 0
    ThreadJoin { semaP(&mysem); }
    ThreadFinish { semaV(&mysem); }

## Slide 20: Revisit Bounded Buffer: Correctness constraints for solution
Correctness Constraints:
  Consumer must wait for producer to fill buffers, if none full (scheduling constraint)
  Producer must wait for consumer to empty buffers, if all full (scheduling constraint)
  Only one thread can manipulate buffer queue at a time (mutual exclusion)
Remember why we need mutual exclusion
  Because computers are stupid
  Imagine if in real life: the delivery person is filling the machine and somebody comes up and tries to stick their money into the machine
General rule of thumb: Use a separate semaphore for each constraint
  Semaphore fullBuffers; // consumer’s constraint
  Semaphore emptyBuffers;// producer’s constraint
  Semaphore mutex; // mutual exclusion

## Slide 21: Bounded Buffer, 3rd cut (coke machine)
Semaphore fullSlots = 0; // Initially, no coke
Semaphore emptySlots = bufSize; // Initially, num empty slots
Semaphore mutex = 1; // No one using machine
Producer(item) { semaP(&emptySlots); // Wait until space semaP(&mutex); // Wait until machine free Enqueue(item); semaV(&mutex); semaV(&fullSlots); // Tell consumers there is // more coke }
Consumer() { semaP(&fullSlots); // Check if there’s a coke semaP(&mutex); // Wait until machine free item = Dequeue(); semaV(&mutex); semaV(&emptySlots); // tell producer need more return item; }
fullSlots signals coke
emptySlots
signals space
Critical sections using mutex protect integrity of the queue

## Slide 22: Discussion about Solution
Why asymmetry?
  Producer does: semaP(&emptyBuffer), semaV(&fullBuffer)
  Consumer does: semaP(&fullBuffer), semaV(&emptyBuffer)
Is order of P’s important?
  Yes! Can cause deadlock
Is order of V’s important?
  No, except that it might affect scheduling efficiency
What if we have 2 producers or 2 consumers?
  Do we need to change anything?
Decrease # of empty slots
Increase # of occupied slots
Increase # of empty slots
Decrease # of occupied slots
Producer(item) { semaP(&mutex); semaP(&emptySlots); Enqueue(item); semaV(&mutex); semaV(&fullSlots); } Consumer() { semaP(&fullSlots); semaP(&mutex); item = Dequeue(); semaV(&mutex); semaV(&emptySlots); return item; }

## Slide 23: Semaphores are good but…Monitors are better!
Semaphores are a huge step up; just think of trying to do the bounded buffer with only loads and stores or even with locks!
Problem is that semaphores are dual purpose:
  They are used for both mutex and scheduling constraints
  Example: the fact that flipping of P’s in bounded buffer gives deadlock is not immediately obvious. How do you prove correctness to someone?
Cleaner idea: Use locks for mutual exclusion and condition variables for scheduling constraints
Definition: Monitor: a lock and zero or more condition variables for managing concurrent access to shared data
  Some languages like Java provide this natively
  Most others use actual locks and condition variables
A “Monitor” is a paradigm for concurrent programming!
  Some languages support monitors explicitly

## Slide 24: Condition Variables
How do we change the consumer() routine to wait until something is on the queue?
  Could do this by keeping a count of the number of things on the queue (with semaphores), but error prone
Condition Variable: a queue of threads waiting for something inside a critical section
  Key idea: allow sleeping inside critical section by atomically releasing lock at time we go to sleep
  Contrast to semaphores: Can’t wait inside critical section
Operations:
  Wait(&lock): Atomically release lock and go to sleep. Re-acquire lock later, before returning.
  Signal(): Wake up one waiter, if any
  Broadcast(): Wake up all waiters
Rule: Must hold lock when doing condition variable ops!

## Slide 25: Monitor with Condition Variables
Lock: the lock provides mutual exclusion to shared data
  Always acquire before accessing shared data structure
  Always release after finishing with shared data
  Lock initially free
Condition Variable: a queue of threads waiting for something inside a critical section
  Key idea: make it possible to go to sleep inside critical section by atomically releasing lock at time we go to sleep
  Contrast to semaphores: Can’t wait inside critical section

## Slide 26: Infinite Synchronized Buffer (with condition variable)
Here is an (infinite) synchronized queue:
lock buf_lock; // Initially unlocked condition buf_CV; // Initially empty queue queue; // Actual queue!
Producer(item) { acquire(&buf_lock); // Get Lock enqueue(&queue,item); // Add item cond_signal(&buf_CV); // Signal any waiters release(&buf_lock); // Release Lock }
Consumer() { acquire(&buf_lock); // Get Lock while (isEmpty(&queue)) { cond_wait(&buf_CV, &buf_lock); // If empty, sleep } item = dequeue(&queue); // Get next item release(&buf_lock); // Release Lock return(item); }

## Slide 27: Mesa vs. Hoare monitors
Need to be careful about precise definition of signal and wait. Consider a piece of our dequeue code:
while (isEmpty(&queue)) { cond_wait(&buf_CV,&buf_lock); // If nothing, sleep } item = dequeue(&queue); // Get next item
  Why didn’t we do this? if (isEmpty(&queue)) { cond_wait(&buf_CV,&buf_lock); // If nothing, sleep } item = dequeue(&queue); // Get next item
Answer: depends on the type of scheduling
  Mesa-style: Named after Xerox-Park Mesa Operating System
    Most OSes use Mesa Scheduling!
  Hoare-style: Named after British logician Tony Hoare

## Slide 28: Hoare monitors
Signaler gives up lock, CPU to waiter; waiter runs immediately
Then, Waiter gives up lock, processor back to signaler when it exits critical section or if it waits again
On first glance, this seems like good semantics
  Waiter gets to run immediately, condition is still correct!
Most textbooks talk about Hoare scheduling
  However, hard to do, not really necessary!
  Forces a lot of context switching (inefficient!)
acquire(&buf_lock);
…
if (isEmpty(&queue)) {
cond_wait(&buf_CV,&buf_lock); } …
release(&buf_lock);
…
acquire(&buf_lock);
…
cond_signal(&buf_CV);
…
release(&buf_lock);
Lock, CPU
Lock, CPU

## Slide 29: Mesa monitors
Signaler keeps lock and processor
Waiter placed on ready queue with no special priority
Practically, need to check condition again after wait
  By the time the waiter gets scheduled, condition may be false again – so, just check again with the “while” loop
Most real operating systems do this!
  More efficient, easier to implement
  Signaler’s cache state, etc still good
acquire(&buf_lock);
…
while (isEmpty(&queue)) { cond_wait(&buf_CV,&buf_lock); } …
lock.Release();
…
acquire(&buf_lock)
…
cond_signal(&buf_CV);
…
release(&buf_lock));
schedule thread (sometime later!)
Put waiting thread on ready queue

## Slide 30: Bounded Buffer – 4rd cut (Monitors, pthread-like)
lock buf_lock = <initially unlocked>
condition producer_CV = <initially empty>
condition consumer_CV = <initially empty>
Producer(item) {
acquire(&buf_lock);
while (buffer full) { cond_wait(&producer_CV, &buf_lock); }
enqueue(item);
cond_signal(&consumer_CV); release(&buf_lock);
}
Consumer() {
acquire(buf_lock);
while (buffer empty) { cond_wait(&consumer_CV, &buf_lock); }
item = dequeue();
cond_signal(&producer_CV);
release(buf_lock);
return item
}
What does thread do when it is waiting?
- Sleep, not busywait!

## Slide 31: Again: Why the while Loop?
MESA semantics
For most operating systems, when a thread is woken up by signal(), it is simply put on the ready queue
It may or may not reacquire the lock immediately!
  Another thread could be scheduled first and "sneak in" to empty the queue
  Need a loop to re-check condition on wakeup
Is this busy waiting?

## Slide 32: OS Library Monitor Pattern: pthreads
// Locks
int pthread_mutex_init(pthread_mutex_t *mutex, const pthread_mutexattr_t *attr);
int pthread_mutex_lock(pthread_mutex_t *mutex);
int pthread_mutex_unlock(pthread_mutex_t *mutex);
// Condition Variables
int pthread_cond_init(pthread_cond_t *cond,
const pthread_mutexattr_t *attr);
int pthread_cond_wait(pthread_cond_t *cond, pthread_mutex_t *mutex);
int pthread_cond_signal(pthread_cond_t *cond);
int pthread_cond_broadcast(pthread_cond_t *cond);

## Slide 33: Readers/Writers Problem
Motivation: Consider a shared database
  Two classes of users:
    Readers – never modify database
    Writers – read and modify database
  Is using a single lock on the whole database sufficient?
    Like to have many readers at the same time
    Only one writer at a time
R
R
R
W

## Slide 34: Basic Structure of Mesa Monitor Program
Monitors represent the synchronization logic of the program
  Wait if necessary
  Signal when change something so any waiting threads can proceed
Basic structure of mesa monitor-based program:
  lock while (need to wait) { condvar.wait(); } unlock do something so no need to wait lock
  condvar.signal();
  unlock
Check and/or update state variables
Wait if necessary
Check and/or update
state variables

## Slide 35: Basic Readers/Writers Solution
Correctness Constraints:
  Readers can access database when no writers
  Writers can access database when no readers or writers
  Only one thread manipulates state variables at a time
Basic structure of a solution:
  Reader() Wait until no writers Access data base Check out – wake up a waiting writer
  Writer() Wait until no active readers or writers Access database Check out – wake up waiting readers or writer
  State variables (Protected by a lock called “lock”):
    int AR: Number of active readers; initially = 0
    int WR: Number of waiting readers; initially = 0
    int AW: Number of active writers; initially = 0
    int WW: Number of waiting writers; initially = 0
    Condition okToRead = NIL
    Condition okToWrite = NIL

## Slide 36: Code for a Reader
Reader() { // First check self into system acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
// Perform actual read-only access AccessDatabase(ReadOnly);
// Now, check out of system acquire(&lock); AR--; // No longer active if (AR == 0 && WW > 0) // No other active readers cond_signal(&okToWrite);// Wake up one writer release(&lock); }
Why Release the Lock here?

## Slide 37: Code for a Writer
Writer() { // First check self into system acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock); // Sleep on cond var WW--; // No longer waiting }
AW++; // Now we are active! release(&lock);
// Perform actual read/write access AccessDatabase(ReadWrite);
// Now, check out of system acquire(&lock); AW--; // No longer active if (WW > 0){ // Give priority to writers cond_signal(&okToWrite);// Wake up one writer } else if (WR > 0) { // Otherwise, wake reader cond_broadcast(&okToRead); // Wake all readers } release(&lock); }
Why Give priority to writers?
Why broadcast() here instead of signal()?

## Slide 38: Simulation of Readers/Writers Solution
Use an example to simulate the solution
Consider the following sequence of operators:
  R1, R2, W1, R3
Initially: AR = 0, WR = 0, AW = 0, WW = 0

## Slide 39: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock)
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 40: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 41: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 42: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
Why release the
lock here???

## Slide 43: Simulation of Readers/Writers Solution
R1 accessing dbase (no other threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 44: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 45: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 46: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 47: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 48: Simulation of Readers/Writers Solution
R1 and R2 accessing dbase
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
Assume readers take a while to access database
  Situation: Locks released, only AR is non-zero

## Slide 49: Simulation of Readers/Writers Solution
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }

## Slide 50: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0

## Slide 51: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 1
W1 cannot start because of readers

## Slide 52: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 0, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 53: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 0, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 54: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 55: Simulation of Readers/Writers Solution
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
R3 comes along (R1, R2 accessing dbase, W1 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
R3 cannot start because of writers (both AW & WW)

## Slide 56: Simulation of Readers/Writers Solution
R1 and R2 accessing dbase, W1 and R3 waiting
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
Status:
R1 and R2 still reading
W1 and R3 waiting on okToWrite and okToRead, respectively

## Slide 57: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 58: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 59: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 60: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 61: Simulation of Readers/Writers Solution
R1 finishes (W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 62: Simulation of Readers/Writers Solution
R1 finishes (W1, R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 63: Simulation of Readers/Writers Solution
R1 finishes (W1, R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 64: Simulation of Readers/Writers Solution
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
R1 signals a writer (W1 and R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
All readers done,
Signal writer W1

## Slide 65: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Receive signal from R1

## Slide 66: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 67: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 68: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 accessing dbase (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 69: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 70: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 71: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 72: Simulation of Readers/Writers Solution
Writer() { acquire(&lock);
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist cond_wait(&okToWrite,&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; release(&lock);
AccessDBase(ReadWrite);
acquire(&lock); AW--; if (WW > 0){ cond_signal(&okToWrite); } else if (WR > 0) { cond_broadcast(&okToRead); } release(&lock); }
W1 signaling readers (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0
No waiting writers,
Signal reader R3

## Slide 73: Simulation of Readers/Writers Solution
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
R3 gets signal (no waiting threads)
AR = 0, WR = 1, AW = 0, WW = 0
Receive signal from W1

## Slide 74: Simulation of Readers/Writers Solution
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
R3 gets signal (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0

## Slide 75: Simulation of Readers/Writers Solution
R3 accessing dbase (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 76: Simulation of Readers/Writers Solution
R3 finishes (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDBase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }

## Slide 77: Simulation of Readers/Writers Solution
R3 finishes (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { acquire(&lock);
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! release(&lock);
AccessDbase(ReadOnly);
acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okToWrite); release(&lock); }
All DONE!
DBase is Idle

## Slide 78: Questions
Can readers starve? Consider Reader() entry code:
  while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist cond_wait(&okToRead,&lock);// Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active!
What if we erase the condition check in Reader exit?
AR--; // No longer active if (AR == 0 && WW > 0) // No other active readers cond_signal(&okToWrite);// Wake up one writer
Further, what if we turn the signal() into broadcast()
AR--; // No longer active cond_broadcast(&okToWrite); // Wake up sleepers
Finally, what if we use only one condition variable (call it “okContinue”) instead of two separate ones?
  Both readers and writers sleep on this variable
  Must use broadcast() instead of signal()

## Slide 79: Use of Single CV: okContinue
Reader() { // check into system acquire(&lock);
while ((AW + WW) > 0) { WR++; cond_wait(&okContinue,&lock); WR--; }
AR++; release(&lock);
// read-only access AccessDbase(ReadOnly);
// check out of system acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okContinue); release(&lock); }
Writer() { // check into system acquire(&lock);
while ((AW + AR) > 0) { WW++; cond_wait(&okContinue,&lock); WW--; }
AW++; release(&lock);
// read/write access AccessDbase(ReadWrite);
// check out of system acquire(&lock); AW--; if (WW > 0){ cond_signal(&okContinue); } else if (WR > 0) { cond_broadcast(&okContinue); } release(&lock); }
What if we turn okToWrite and okToRead into okContinue (i.e. use only one condition variable instead of two)?

## Slide 80: Use of Single CV: okContinue
Reader() { // check into system acquire(&lock);
while ((AW + WW) > 0) { WR++; cond_wait(&okContinue,&lock); WR--; }
AR++; release(&lock);
// read-only access AccessDbase(ReadOnly);
// check out of system acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_signal(&okContinue); release(&lock); }
Writer() { // check into system acquire(&lock);
while ((AW + AR) > 0) { WW++; cond_wait(&okContinue,&lock); WW--; }
AW++; release(&lock);
// read/write access AccessDbase(ReadWrite);
// check out of system acquire(&lock); AW--; if (WW > 0){ cond_signal(&okContinue); } else if (WR > 0) { cond_broadcast(&okContinue); } release(&lock); }
Consider this scenario:
R1 arrives
W1, R2 arrive while R1 still reading  W1 and R2 wait for R1 to finish
Assume R1’s signal is delivered to R2 (not W1)

## Slide 81: Use of Single CV: okContinue
Reader() { // check into system acquire(&lock);
while ((AW + WW) > 0) { WR++; cond_wait(&okContinue,&lock); WR--; }
AR++; release(&lock);
// read-only access AccessDbase(ReadOnly);
// check out of system acquire(&lock); AR--; if (AR == 0 && WW > 0) cond_broadcast(&okContinue); release(&lock); }
Writer() { // check into system acquire(&lock);
while ((AW + AR) > 0) { WW++; cond_wait(&okContinue,&lock); WW--; }
AW++; release(&lock);
// read/write access AccessDbase(ReadWrite);
// check out of system acquire(&lock); AW--; if (WW > 0 || WR > 0){ cond_broadcast(&okContinue); } release(&lock); }
Need to change to broadcast()!
Must broadcast() to sort things out!

## Slide 82: Can we construct Monitors from Semaphores?
Locking aspect is easy: Just use a mutex
Can we implement condition variables this way?
  Wait(Semaphore *thesema) { semaP(thesema); }
  Signal(Semaphore *thesema) { semaV(thesema); }
  Doesn’t work: Wait() may sleep with lock held
Does this work better?
  Wait(Lock *thelock, Semaphore *thesema) { release(thelock); semaP(thesema); acquire(thelock); } Signal(Semaphore *thesema) {
  semaV(thesema); }
  No: Condition vars have no history, semaphores have history:
    What if thread signals and no one is waiting? NO-OP
    What if thread later waits? Thread Waits
    What if thread V’s and noone is waiting? Increment
    What if thread later does P? Decrement and continue

## Slide 83: Construction of Monitors from Semaphores (con’t)
Problem with previous try:
  P and V are commutative – result is the same no matter what order they occur
  Condition variables are NOT commutative
Does this fix the problem?
  Wait(Lock *thelock, Semaphore *thesema) { release(thelock); semaP(thesema); acquire(thelock); } Signal(Semaphore *thesema) { if semaphore queue is not empty semaV(thesema); }
  Not legal to look at contents of semaphore queue
  There is a race condition – signaler can slip in after lock release and before waiter executes semaphore.P()
It is actually possible to do this correctly
  Complex solution for Hoare scheduling in book
  Can you come up with simpler Mesa-scheduled solution?

## Slide 84: Mesa Monitor Conclusion
Monitors represent the synchronization logic of the program
  Wait if necessary
  Signal when change something so any waiting threads can proceed
Typical structure of monitor-based program:
  lock while (need to wait) { condvar.wait(); } unlock do something so no need to wait lock
  condvar.signal();
  unlock
Check and/or update state variables
Wait if necessary
Check and/or update
state variables

## Slide 85: C-Language Support for Synchronization
C language: Pretty straightforward synchronization
  Just make sure you know all the code paths out of a critical section
  int Rtn() { acquire(&lock); … if (exception) { release(&lock); return errReturnCode; } … release(&lock); return OK; }
  Watch out for setjmp/longjmp!
    Can cause a non-local jump out of procedure
    In example, procedure E calls longjmp, poping stack back to procedure B
    If Procedure C had lock.acquire, problem!
Proc A
Proc B
Calls setjmp
Proc C
acquire(&lock)
Proc D
Proc E
Calls longjmp
Stack growth

## Slide 86: Concurrency and Synchronization in C
Harder with more locks
void Rtn() { lock1.acquire(); … if (error) { lock1.release(); return; }
…
lock2.acquire();
…
if (error) {
lock2.release()
lock1.release();
return;
}
…
lock2.release();
lock1.release(); }
Is goto a solution???
void Rtn() { lock1.acquire(); … if (error) { goto release_lock1_and_return; }
…
lock2.acquire();
…
if (error) {
goto release_both_and_return;
}
…
release_both_and_return:
lock2.release();
release_lock1_and_return:
lock1.release(); }

## Slide 87: C++ Language Support for Synchronization
Languages with exceptions like C++
  Languages that support exceptions are problematic (easy to make a non-local exit without releasing lock)
  Consider:
  void Rtn() { lock.acquire(); … DoFoo(); … lock.release(); } void DoFoo() { … if (exception) throw errException; … }
  Notice that an exception in DoFoo() will exit without releasing the lock!

## Slide 88: C++ Language Support for Synchronization (con’t)
Must catch all exceptions in critical sections
  Catch exceptions, release lock, and re-throw exception: void Rtn() { lock.acquire(); try { … DoFoo(); … } catch (…) { // catch exception lock.release(); // release lock throw; // re-throw the exception } lock.release(); } void DoFoo() { … if (exception) throw errException; … }

## Slide 89: Much better: C++ Lock Guards
#include <mutex>
int global_i = 0;
std::mutex global_mutex;
void safe_increment() {
std::lock_guard<std::mutex> lock(global_mutex);
…
global_i++;
// Mutex released when ‘lock’ goes out of scope
}

## Slide 90: Python with Keyword
More versatile than we show here (can be used to close files, database connections, etc.)
lock = threading.Lock()
…
with lock: # Automatically calls acquire()
some_var += 1
…
# release() called however we leave block

## Slide 91: Java synchronized Keyword
Every Java object has an associated lock:
  Lock is acquired on entry and released on exit from a synchronized method
  Lock is properly released if exception occurs inside a synchronized method
  Mutex execution of synchronized methods (beware deadlock)
class Account { private int balance; // object constructor public Account (int initialBalance) { balance = initialBalance; } public synchronized int getBalance() { return balance; } public synchronized void deposit(int amount) { balance += amount; } }

## Slide 92: Java Support for Monitors
Along with a lock, every object has a single condition variable associated with it
To wait inside a synchronized method:
  void wait();
  void wait(long timeout);
To signal while in a synchronized method:
  void notify();
  void notifyAll();

## Slide 93: Conclusion
Semaphores: Like integers with restricted interface
  Two operations:
    P(): Wait if zero; decrement when becomes non-zero
    V(): Increment and wake a sleeping task (if exists)
    Can initialize value to any non-negative value
  Use separate semaphore for each constraint
Monitors: A lock plus one or more condition variables
  Always acquire lock before accessing shared data
  Use condition variables to wait inside critical section
    Three Operations: Wait(), Signal(), and Broadcast()
Monitors represent the logic of the program
  Wait if necessary
  Signal when change something so any waiting threads can proceed
  Monitors supported natively in a number of languages
Readers/Writers Monitor example
  Shows how monitors allow sophisticated controlled entry to protected code